SAFETY INSPECTION STANDARDS

OXYGEN AND ACETYLENE GASES  :

ุ	Fix cylinders to a carrier, or to a fixed object with chain or an approved clamp (Rope or wire is not acceptable).

ุ	Always closes cylinder valves when the equipment is not in use. No pressure should be left in the lines when stored.

ุ	Keep oil and grease from cylinder valves, hoses, and cutting equipment

ุ	Cylinders should be upright position when in use or storage

ุ	Keep clear of sparks, flame, or electric welding sparks

ุ	Hose should be in good condition, free of oil and grease and the outer sheath should not be abraded or burnt,

ุ	The hoses should be neatly rolled up when stored.

ุ	Empty cylinders marked and returned to warehouse, not stored in work area.

ุ	Never use acetylene at a pressure over 28 psi. Backflash arrestors (color coded same as hoses) must be used on both bottles.

ุ	Cutting torches must be kept in good condition (not dented cracked or damaged with “cutting splatter).  Tips must be clean to allow even cutting. Must be lit with a friction lighter.

ELECTRICAL ROOM  :

ุ	Should meet general housekeeping standards.

ุ	The entrances to electrical rooms should be clear of all obstructions and the door should automatically close. The door should not be lockable.

ุ	There should be clear access to all electrical panels of 1.5 meters with no obstructions.

ุ	The smoke detector should be checked for operation with test smoke canisters. (wait to see if there is any

ุ	response from the control room).

ุ	Electrical panels should not have any missing or open covers or openings (except grilled or screened vents).

ุ	Clear of all materials except plans that should be stored on a table or desk (there should not be an accumulation of spare parts, nuts, bolts, etc stored in the control room). High Voltage switchgear properly covered is acceptable as long as it does not interfere with access to the panels or walkways.

ุ	No materials or accumulation of dust should be evident on top of electrical panels.

ุ	All cable entrances to the room should be sealed with a non flammable material.

ุ	All control panels should be clean an clearly marked (ensure the panels are free of dust, oil and grease and the

ุ	markings show what device is controlled by the panel).

ุ	All doors on panels should be secured and unable to be opened by unauthorized personnel.

ุ	All power switchboards should not be able to be opened until the mains supply has been shut off on that panel.

ุ	Fire Extinguishers must comply with fire extinguisher standards

ุ	Lighting should comply with lighting standards

ุ	All flammable material must be removed. Garbage containers must have air tight lids and all material removed

ุ	when work is complete.

LOCAL PANELS, ELECTRICAL DEVICES AND CONTROLS IN THE WORK AREA  :

ุ	Must be securely fastened to a permanent structure such as walls or steel beams (cable ties, rope or wire are not

ุ	adequate fastenings).

ุ	Must be sealed against dust and water (check for holes or cracks on all sides of panel (the bottom may have a drain hole which is acceptable). Also check for loose electrical cables entering the device.

ุ	Must be properly locked or sealed to prevent unauthorized access.

ุ	Must be clear of obstructions that prevent easy access ( An area of at least 1.5 meters around the electrical panel must be clear of all obstructions)

ุ	Must be clean and clearly marked ( there should be no accumulation of dirt, grease  or oil on the panel. The

ุ	markings should identify the device it operates and the location of the power source).

LIGHTING  :

ุ	Battery operated emergency lighting (where installed)  must have clear labeling for testing and must be tested for

ุ	operation.

ุ	Must be adequate for the task being performed ( ask operator for his opinion).

ุ	Must be functional  (check switches to ensure the lights work).

ุ	Must be securely fastened (rope, wire and cable ties are not acceptable fastening).

ุ	Reflectors and covers must be clean and in good condition (not cracked or discolored)

CABLE TRAYS  :

ุ	Clear of accumulated rubbish (should not have an accumulation of grease, oil, rags, rocks or mud covering the

ุ	cables)

ุ	Should not be rusted or corroded.

ุ	Cables secure and orderly (wire or rope are not acceptable cable clamps).

ุ	Covered where susceptible to falling rocks, oil or other materials that could damage the cable.

ุ	Properly secured with brackets, not supported with rope or other temporary measures.

ุ	Nothing should be hanging  or supported by the tray, except electrical cables(temporary hoses, pipes or buckets

ุ	should not be supported from the tray).

ELECTRICAL WIRING  :

ุ	Must be run in electrical cable trays or securely fastened every 1.5 meters by proper cable clamps (cable ties,

ุ	rope or wire is not acceptable).

ุ	Must be terminated using a proper connector that secures the cable from being pulled out and prevents access

ุ	of water or dust.

ุ	Must not have anything supported from the cable or conduit (check that hoses, pipes, buckets are not

ุ	suspended from electrical wires).

ุ	Must not be dented, bent or have the outer protection damaged in any way.

ุ	Must be properly tagged where it enters any electrical device (tags identifying the cable must be readable).

ุ	All wiring must be terminated in an electrical device or junction box. Where an electrical device has been temporarily removed the wiring must be taped and tagged.

ุ	Electrical and communication cords must be clearly tagged as to the last inspection (within the last 6 months). Tag color for date is as follows Jan-Jun 1998 = red, Jul-Dec 1998 = blue, Jan-Jun 1999 = green, Jul- Dec 1999 = yellow.

MOTORS  :

ุ	Must be clearly marked for the location of the electrical shut off.

ุ	Fan guards must be secured to motor and clear of obstructions.

ุ	Must be clean of oil, grease, rocks and mud buildup .

ุ	Junction box must be sealed and properly secured with all bolts in place (wire, rope and cable ties are not acceptable).

ุ	Must not be rusted or corroded

PORTABLE WELDING MACHINES  :

ุ	All cables must be rolled up and hung from appropriate supports. Cables must be free from damage to outer protection.

ุ	Connections must be securely fastened with no visible damage or wear.

ุ	Stinger must not have any cracks or damage to the insulation on the handle (it should also be free of mud, oil and grease).

ุ	Control panel must be clean and all indicators and instructions clearly visible and in working order.

ุ	Engine covers must latch securely in place and must be able to be latched in the open position.

ุ	Battery must be securely fastened in place, the battery caps in place and the battery clean (free from dirt, oil, grease and mud).

ุ	Engine should be free of oil leaks and clear of mud or oil buildup.

ุ	Radiator should be free of water leaks and must be clear of oil or mud buildup. The pressure cap must be securely in place (do not attempt to touch the cap if the radiator is warm).

ุ	Radiator fan must be protected from access by hands when the covers are open.

ุ	Welding Machine must be located in a dry location away from potential sources of water or slurry.

TRANSFORMERS  :

ุ	Must be protected from access by a fence (see Fencing standards).

ุ	Must be clean and free from any oil leaks (especially check cooling fins).

ุ	Should be free of rust or corrosion.

ุ	Bund (containment area) should not have any oil in evidence, nor should there be any materials stored in the area or garbage present.(See housekeeping standard).

ุ	Bund Drain, if applicable, must be closed.

COMMUNICATIONS (RADIOS & TELEPHONES)  :

ุ	Must be operational.

ุ	Must be in a clear, accessible area.

ุ	Must have a list of radio channels and a telephone book present and have emergency numbers clearly visible.

ุ	All wiring must be neatly secured and in good order.

CONTROL ROOMS  :

ุ	Should meet general housekeeping standards.

ุ	Items like ear plugs, lockout tags, reference, operational manuals and plans may be stored in the control room.

ุ	Control panels must be clean and not have any items stored on them (free of dirt, water , oil, grease and coffee

ุ	cups)

ุ	All controls should be clearly labeled as to the device they control.

ุ	All Holes in the room should be properly sealed with non flammable materials.	.

LADDERS   :

ุ	Must be in good structural condition manufactured to proper standards (no loose or dented rails or rungs).

ุ	Must have proper non skid feet.

ุ	When in us they must be assembled in the proper 4 to 1 angle.

ุ	Must be stored on hooks in a manner that will prevent sagging.

ุ	Must be tied in position while in use or supported by a second person.

ุ	All work on electrical equipment must be done from a non conductive ladder (either unpainted wood or fiberglass).

STORAGE OF LUBRICANTS OR SOLVENTS IN BARRELS  :

ุ	Full barrels not in use must be stored in properly bunded areas. Drums must be protected or tilted to prevent accumulation of water on the top.

ุ	Barrels are  in use must be mounted over a drip tray. Drip trays under units should be clear of oil.

ุ	There should not be an accumulation of empty barrels in work areas.

ุ	Bunds should be clear of oil or water.

ุ	All valves on barrels and bunds should be spring loaded to automatically close..

ุ	Fire fighting equipment must be within close proximity of oil storage areas, easily accessible and meet standards for fire extinguishers/ fire fighting equipment.

HYDRAULIC OPERATED EQUIPMENT  :

ุ	Fire sprinkler system must be mounted above unit with a heat shield to deflect heat to spray nozzle.

ุ	Check for any damaged hoses (hose should not be kinked or have any visible damage to the outer sheath or connections.

ุ	All hydraulic units must be clear of any accumulation of any dirt or oil.

ุ	All hydraulic units must be bunded to prevent the spillage of oil and bunds must be free of any oil, water or accumulation of dirt or foreign material.

ุ	Check for any leaking around couplings fittings or shafts.

ุ	Any drive couplings or rotating components must have guards securely fastened in place.

ุ	All valves on bunds should be spring loaded to automatically close..

OIL AND WATER COOLERS   :

ุ	Fire sprinkler system must be mounted above hydraulic units with a heat shield to deflect heat to spray nozzle.

ุ	Check for any damaged hoses (hose should not be kinked or have any visible damage to the outer sheath or connections.

ุ	All fans and rotating equipment must be protected by securely fastened guarded. There should not be any accumulation of oil or dirt on the fan blades.

ุ	There should not be any noticeable vibration while operating.

ุ	Radiators must be clean of any accumulation of dirt and oil and there must be no visible leaks.

ุ	All hydraulic units must be clear of any accumulation of any dirt or oil.

ุ	All hydraulic units must be bunded to prevent the spillage of oil and bunds must be free of any oil, water or accumulation of dirt or foreign material.

ุ	All valves on bunds should be spring loaded to automatically close..

GENERAL HOUSEKEEPING--- BULK FUEL, CHEMICAL LOADING AND STORAGE AREAS:

ุ	There should not be an accumulation of empty barrels in work areas.

ุ	Bunds should be clear of oil or water.

ุ	All valves on bunds should be chained closed or spring loaded to automatically close..

ุ	Fire fighting equipment must be within close proximity of oil storage areas, easily accessible and meet standards for fire extinguishers/ fire fighting equipment.

ุ	Check for leaks from tanks, pies and valves.

GENERAL HOUSEKEEPING--- OUTDOORS:

ุ	Signage and posters should be up do date, relevant, and well maintained.

ุ	All traffic control signs should be followed (No Parking, Speed, etc.) {Speed gun should be used on this tour and offenders pulled over and explained their infraction}

ุ	Should be clear of any foreign items, cigarette butts, garbage, paper waste, scrap metal, etc.

ุ	There should not be any evidence of oil or grease spills.

ุ	Dead foliage (dead trees, piles of grass, etc.) should not be evident.

GENERAL STANDARDS----EMPLOYEES

ุ	General

ุ	Ensure that employees are wearing the proper personal protective equipment (Hard hats, hard toed boots, safety glasses, ands specialized safety equipment as noted under work areas as noted.

ุ	Must wear protective gloves when handling equipment.

ุ	Operating oxygen/acetylene equipment

ุ	Employees must have welding and cutting ticket 4.33 (check with operator)

ุ	Cutting goggles with a colored lens and gloves must be used when operating cutting and gas welding equipment.

ุ	Operating Electric Arc equipment

ุ	Employees must have welding and cutting ticket 4.33 (check with operator)

ุ	Must wear protective leather apron

ุ	Must wear protective leather gloves

ุ	Etc. Etc.

GENERAL HOUSEKEEPING--- SHOPS AND OPERATIONAL BUILDINGS:

ุ	Signage and posters should be up do date, relevant and well maintained.

ุ	Room should be clear of all graffiti and non operational posters and notices (no pornography or suggestive calendars).

ุ	All floors must be clear of any accumulation of dirt, oil, grease or materials that could create a tripping or slipping hazard.

ุ	Grated floors must not have material stuck in the grating that could create a tripping hazard.

ุ	Walkways must clearly marked and should be free of any obstacles or collection of materials.

ุ	Aprons and approaches to buildings should be clearly marked for traffic flow and No Parking areas clearly identified and enforced.

ุ	Garbage containers should be clearly marked (in English and Pidgin) as to type of scrap that is acceptable, covered and not overflowing.

ุ	Cables, fabric slings and chains should be  in good condition (not obvious wear or damage). If in doubt talk to supervisor.

ุ	All tools should be kept in a neat and orderly fashion (tools not in use should not be left on the floor or work benches.

ุ	Parts for rebuild should be marked with standard tags and components waiting for parts stored in a neat manner.

ุ	Welding rods should be stored in drying ovens if the containers have been opened.

ุ	There should not be any welding rod ends (butts) laying on the floor or work area.

ุ	Service manuals stored in proper locations.

ุ	Flammable liquids stored in containers purposely designed and labeled.

ุ	Racks and work benches in neat order. (not cluttered with parts, rags, tools, etc.).

ุ	Hydraulic equipment ports should be plugged to prevent contamination when not in use.

ุ	Rags stored in a container designed for the purpose and clearly marked (A garbage can with a lid is suitable).

ุ	There should not be an accumulation of warehouse parts in the shop, laying on wall purlins or stuck in corners.

ุ	Cleaning solutions must be stored in properly labeled containers. All hoses and cables must be rolled up and neatly stored when not in use.

ุ	All air couplings in use must have safety wires installed.

ุ	Blocking and support stands must be stored in a neat orderly manner.

GENERAL HOUSEKEEPING--- OFFICES AND CONTROL ROOMS:

ุ	Garbage containers should have secure lids and not overflowing.

ุ	Must be clean and free of dust and foreign material.

ุ	Desks and chairs should be in good working order (ask the opinion of the operator).

ุ	Windows should be clean and in good working order (louvers operational, no cracks and clear visibility)

ุ	Room should be clear of all graffiti and on operational posters and notices (no pornography or suggestive

ุ	calendars).

ุ	Room should have all holes or unused opening sealed with non-combustive material.

ุ	Signage and posters should be up do date, relevant and well maintained

ุ	They must meet General Standards for Tea Rooms if they are used for this function.

GENERAL HOUSEKEEPING--- WASHROOMS  :

ุ	Toilets should be spotlessly clean with no evidence of leaks from tap, water tank or drain, There should be no evidence of the water continuously running in the bowl. Toilet seats should be clean and securely attached to the toilet.

ุ	Sinks should be spotlessly clean with no leaks evident from faucets or drain.

ุ	Soap and paper towels available. (Liquid soap dispenser should not leak).

ุ	Spare supplies should not be stored in the washrooms.

ุ	Lighting fixtures should meet lighting standards.

ุ	Floors clean (no dirt, oil, grease or paper visible) and in good condition (floor covering not ripped or loose).

ุ	Garbage containers should be in good condition and not dirty or overflowing.

ุ	Windows and doors to be clean and louvers functional (No windows should be cracked or broken).

ุ	Room should be clear of all graffiti (no pornography or suggestive calendars).

GENERAL HOUSEKEEPING--- DONGAS:

ุ	Common room should be general standards for a tea room.

ุ	Toilets should be spotlessly clean with no evidence of leaks from tap, water tank or drain, There should be no evidence of the water continuously running in the bowl. Toilet seats should be clean and securely attached to the toilet.

ุ	Sinks should be spotlessly clean with no leaks evident from faucets or drain.

ุ	Lighting fixtures should meet lighting standards.

ุ	Floors clean (no dirt, oil, grease or paper visible) and in good condition (floor covering not ripped or loose).

ุ	Garbage containers should be in good condition and not dirty or overflowing.

ุ	Windows and doors to be clean and louvers functional (No windows should be cracked or broken).

ุ	Common rooms and Bedrooms should be clear of all graffiti (no pornography or suggestive calendars).

ุ	Common room should not have an accumulation of papers  and books unless they are neatly on shelves.

ุ	Furniture should be clean, not badly worn and in solid condition

GENERAL HOUSEKEEPING--- MESS FACILITIES:

ุ	Windows and doors to be clean and louvers functional (No windows should be cracked or broken).

ุ	Room should be clear of all graffiti (no pornography, suggestive calendars or suggestive cartoons).

ุ	Lighting fixtures should meet lighting standards.

ุ	Floors clean (no dirt, oil, grease or paper visible) and in good condition (floor covering not ripped or loose).

ุ	Washrooms should meet general standards for washrooms.

ุ	Food serving and preparation area should be spotlessly clean.

ุ	Tables and chairs should be clean and solid with no visible damage.

ุ	Garbage storage areas should be clear of all materials. Containers should have securely fitting lids and should not be overflowing.

ุ	There should be no unusual odors generated from the drains, garbage areas and septic systems.

ุ	Chefs and food servers should be cleanly dressed and neat in appearance.

GENERAL HOUSEKEEPING--- RECREATIONAL BUILDINGS:

ุ	Windows and doors to be clean and louvers functional (No windows should be cracked or broken).

ุ	Room should be clear of all graffiti (no pornography or suggestive calendars).

ุ	Lighting fixtures should meet lighting standards.

ุ	Floors clean (no dirt, oil, grease or paper visible) and in good condition (floor covering not ripped or loose).

ุ	Washrooms should meet general standards for washrooms.

GENERAL HOUSEKEEPING--- TEA ROOMS:

ุ	Garbage containers should have secure lids and not overflowing.

ุ	Must be clean and free of dust and foreign material.

ุ	Chairs and tables should be in good working condition (solid, no signs of damage or excessive wear.

ุ	Windows should be clean and in good working order (louvers operational, no cracks and clear visibility)

ุ	Room should be clear of all graffiti and non operational posters and notices (no pornography, suggestive calendars or suggestive cartoons).

ุ	Signage and posters should be up do date, relevant and well maintained

ุ	All appliance must be clean and free of any food build up.

ุ	Doors on microwaves and refrigerators must seal and latch properly.

ุ	Any food should be in sealed containers and preferably in a refrigerator, if available (this

ุ	includes coffee making materials).

GENERAL HOUSEKEEPING--- BULLETIN BOARDS:

ุ	Signage and posters should be up do date, relevant and well maintained.

ุ	Room should be clear of all graffiti and non operational posters and notices (no pornography, suggestive calendars or suggestive cartoons).

GENERAL HOUSEKEEPING--- FIRE EXTINGUISHERS AND FIRE FIGHTING EQUIPMENT:

Portable fire extinguishers must be securely mounted with appropriate brackets that allow easy removal.

There must be a clear access to the fire extinguisher of at least 1.5 meters.

Gauge should read OK or in the ‘green’ portion of the gauge.

The safety pin should be wired into place with easily breakable wire.

Should be clearly identified as to use (Electrical, oil, general) and be in an appropriate place (fire extinguisher for electrical should not be mounted in an oil bund).

ุ	Fire extinguishers must be clearly tagged as to the last inspection (within the last 6 months). Tag color for date is as follows Jan-Jun 1998 = red, Jul-Dec 1998 = blue, Jan-Jun 1999 = green, Jul- Dec 1999 = yellow.

ุ	Water monitors must be mounted in such a way as to allow easy access and egress and their field of fire should not be obstructed.

ุ	Water monitors should be permanently connected to a fire line for instant use.(unless they are a portable model).